## Slide 1: Project 3 Tutorial
CMP (Cache_Memory_Pagetable)
Notes: 今天由我講解implement memory hierarchy

## Slide 2: Translation with a TLB
CPU
Cache
TLB
Main Memory
PTE
Disk
VA
PA
TLB Miss
PT Miss
Page Fault
PT Hit
Swap in
Cache
Hit
Cache
Miss
Notes: Virtual Memory 的機制

## Slide 3: Virtual Memory in Modern System
Core
D-TLB
I-TLB
D-Cache
I-Cache
Memory
Page Table
Disk
Notes: Virtual Memory 在我們現在系統上的架構

## Slide 4: CMP Architecture (1/2)
CPU
i-tlb
i-cache
i-mem
i-page
table
i-disk
(iimage.bin)
VA(PC)
hit
miss
miss
(miss)
swap
hit
miss
hit
hit
d-tlb
d-page
table
miss
hit
d-cache
hit
d-mem
miss
hit
miss
d-disk
(dimage.bin)
load/store
Instruction
hit
(miss)
swap
Notes: CMP指令跟資料hit/miss的流程圖, 幫助同學在實作的時候更了解tlb cache pt之間的關係

## Slide 5: CMP Architecture (2/2)
TLB | Page table | Cache | Solution
Hit | Hit | Hit | 
Hit | Hit | Miss | Search memory  update cache
Miss | Hit | Hit | Update TLB
Miss | Hit | Miss | Update TLB search memory  update cache
Miss | Miss | Miss | Swap  update PageTable  update TLB  update cache
TLB & Memory adopt LRU replacement policy
Cache adopt bits-pseudo LRU replacement policy

## Slide 6: LRU
Several Implementations
  Use variable to record time (cycle)
Cache Miss =>Replace least recently used block
variable
35
33
8
11
15
8
5
Only in simulation, it is infeasible for real hardware
How is an LRU cache implemented in a CPU?
Notes: 最近最少被使用

## Slide 7: Bits-pseudo LRU (1/2)
MRU, to record the usage status of each cache block
Cache Miss =>Replace the lowest indexed block of MRU=0
Cache Miss
Notes: MRU 記錄每一個block的使用狀況
從最小block的MRU開始找等於0的做替換

## Slide 8: Bits-pseudo LRU (2/2)
there is one last block with MRU=0
Cache Miss
Reset others, except the one just replaced
Notes: 除了將index 4 的MRU改為1 而且reset其他的MRU為0

## Slide 9: Same & Difference
Same single cycle execution as Project 1.
No more error handler. (no error_dump.rpt)
Error | behavior | handle
Write reg. 0 | $0 still maintain 0 | Not print
Overwrite HI-LO registers | Store wrong result | Not print
Num. Overflow | Store wrong result | Not print
Mem. misalignment | Invalid design test case (program will crash then stop) | 
Mem. Overflow |  | 

## Slide 10: Input
Same input file format
  iimage.bin
  diimage.bin
Invalid testcase
  i-memory & d-memory address overflow
  i-memory & d-memory misaligned
  Simulation cycles over 500,000

## Slide 11: Output
snapshot.rpt
  register file content at each cycle
report.rpt
  total number of TLB/ PageTable/ Cache hits/misses

## Slide 12: Trace.rpt
It is not to be graded , just help you to know what happens in each cycle
Format:
Cycle, Instruction :Instruction hit location ;Data hit location

## Slide 13: Execution Parameter
Executable is configurable
All size are in number of bytes.
All size related parameters should be of 2n, n > 1.
When just execute the program (“./CMP”):
  The program should be default configuration:
  (P1, P2, …, P10) = (64, 32, 8, 16, 16, 4, 4, 16, 4, 1)
Intr.
Data
Intr.
Data
cache
memory
page
Data
Intr.
Notes: 可配置
設定mem page cache size跟associativity

## Slide 14: Execution Parameter Detail
./CMP [P1] [P2] [P3] [P4] [P5] [P6] [P7] [P8] [P9] [P10]
  [P1]: The I-memory size
  [P2]: The D-memory size
  [P3]: The page size of I-memory
  [P4]: The page size of D-memory
  [P5]: The total size of I-cache
  [P6]: The block size of I-cache
  [P7]: The set associativity of I-cache
  [P8]: The total size of D-cache
  [P9]: The block size of D-cache
  [P10]: The set associativity of D-cache

## Slide 15: Submission
CMP
  testcase
    iimage.bin
    dimage.bin
  simulator
    CMP
    makefile
    XXX.c …etc
1st Submission: 2017/06/03
2nd Submission: 2017/06/10
Tar on this folder
(capital )
（capital )

## Slide 16: Evaluation
For open, hidden, and student test case, TA will use 3 config. to evaluate.
  default configuration
  two other configurations
Grading:
  10% discount if you fail one of them（九折）
  19% discount if you fail both of them（九折*九折）
  0 point if you fail all of them

## Slide 17: Bonus
If you hand in your homework before 5/20 (two weeks before 1st submission), you can get additional 14% bonus.
The bonus point will deduct 1% everyday.
5/20 | 5/21 | 5/22 | 5/23 | 5/24 | 5/25 | 5/26
14% | 13% | 12% | 11% | 10% | 9% | 8%
5/27 | 5/28 | 5/29 | 5/30 | 5/31 | 6/1 | 6/2
7% | 6% | 5% | 4% | 3% | 2% | 1%

## Slide 18: Modularization
CMP
main
mem
processor
reg
Notes: 模組化的格式 同學可以參考一下

## Slide 19: Project 2 Demo time
5/12 fill in the demo time (18:00)
5/14 mother’s day
5/19 project 2 demo